## Slide 1: Methods of Industrial Mathematics
Extended LTCC Advanced Course – Feb-Mar 2018
John Curtis, UCL Mathematics Department
© British Crown Owned Copyright 2018/AWE.

## Slide 2: Session 1
A personal overview of where mathematics is applied in industry.
Some problems of applied dynamics resulting in ordinary differential equations.
Solution by explicit Runge-Kutta methods.
Modelling friction.

## Slide 3: Industrial Mathematics Encountered by JC
INDUSTRIAL MATHEMATICS USED BY JC
MECHANICS
CHEMISTRY
SIMULATION
ELECTROMAGNETIC THEORY
CONTROL THEORY
SIGNAL PROCESSING
OPTIMISATION
Arrows join most of the above subjects
N.B. No attempt at definitive list of Industrial Mathematics , e.g. Image Processing, Big Data, Formal Methods, Financial Mathematics are missing.
STATISTICS
PROBABILITY
NUMERICAL ANALYSIS
APPLIED PHYSICS
ENGINEERING
HEAT TRANSFER

## Slide 4
Hilbert
Space

## Slide 5: Mechanics Applications
Dynamics of rigid bodies as applied to spacecraft
Vehicle Dynamics and Flow
Mechanics of solids, including plastic flow of jets as applied in oil well perforators
Continuum and fluid mechanics:
  Jet formation
  Jet dynamics and break-up
  Jet penetration
  Impact and resulting deformation including shocks
  Explosive safety applications including fragmentation

## Slide 6: Heat Transfer and Diffusion Applications
Conduction in, and reaction of, explosives
Minimisation of heat loss
Diffusion modelling

## Slide 7: Simulation Examples
Spacecraft mission modelling
Mechanics – oil well perforators
Chemical reactions
Ageing of powders
Traffic modelling
Staff Modelling
Top Dog
Manager 1
Minion 1
Minion 2
Manager 2
Minion 3
The CEO
Middle Management
Workers

## Slide 8: Numerical Modelling
Nonlinear ODEs
Finite difference methods for boundary-value problems
The finite element method

## Slide 9: Optimisation
Optimisation of speed, momentum and energy of an explosively projected plate.
Minimisation of heat loss
Maintaining orthogonality of axes

## Slide 10: Spacecraft Dynamics Frame Definitions
Simplest satellite is a rigid body.
Let the c. of g. be at position in fixed co-ordinates.
Let be body-fixed (i.e. translating and rotating) co-ordinates.

## Slide 11: Translation
The 3 equations governing the translational dynamics are:
where are gravitational forces and
are thrusts.

## Slide 12: Body Frame Rotation
Let be unit vectors in the spacecraft body frame.
Then their rates of change are given by the vector equation:
Here is the angular velocity vector.
These comprise 9 equations in the individual components.

## Slide 13: Spacecraft Dynamics – Angular Momentum
The equations of angular momentum govern the rotation of the spacecraft.
These are the Euler equations – traditionally introduced in modelling the spinning top. [There is much theory on this – cf. Goldstein for a comprehensive treatment]
It is convenient to make the spacecraft fixed axes coincident with the principal axes of inertia so that the inertia tensor is diagonalized.
Under these circumstances the Euler equations simplify to the following:

## Slide 14: Euler Equations
,
,
.
N.B. Here the principal moments of inertia , components of total applied torque , and components of angular velocity are all in the body fixed co-ordinate system.

## Slide 15: Reduction of Translation Equations to First Order Equations
This is very easily accomplished by writing
,
replacing by on the left-hand side of the translation equation,
and replacing by , and other derivatives where necessary using the other equations as above.
Now there are 6 equations associated with translation.

## Slide 16: Spacecraft Dynamics Summary
6 translation equations,
9 frame rotation equations,
3 Euler equations.
18 equations in all!
There are 18 states satisfying 18 ordinary differential equations (ODEs) of the form:
.
I could rest my case here that fairly simple – at least straightforward - ODEs in particular and mathematics in general are vital in industry, as industry builds every spacecraft! It is big business – just ask BAE or Lockheed Martin if they’d mind awfully giving this business up.

## Slide 17: Spacecraft I Have Modelled
While with British Aerospace back in 1979-1983.
Early electronic computer screens.
Some additional maths needed in some cases – friction and beam theory.
Giotto comet rendezvous
ESA/Giotto

## Slide 18: Ulysses Mission
Ulysses Mission (formerly International Solar Polar Mission).
Out to Jupiter to use its gravitational field to come out of the Solar System ecliptic plane and fly over the poles of the sun.
Spacecraft rotating at 5 rpm carrying a 5 m axial flexible beam antenna and two radial 30 m long wire booms. These complicated the Euler equations a fair bit as you may guess!
ESA/Ulysses

## Slide 19: Hubble Space Telescope
Modelled the dynamics and control system of the solar arrays.
Included modelling the beam-like deformation of the array as it turned
and hysteresis torques from twisting the cables to the solar arrays.
ESA/Hubble

## Slide 20: Images from Hubble!
NASA Hubble Telescope Compilation: ©1997 Finley Holiday Film Corporation

## Slide 21
NASA Hubble Telescope Compilation: ©1997 Finley Holiday Film Corporation

## Slide 22
NASA Hubble Telescope Compilation: ©1997 Finley Holiday Film Corporation

## Slide 23: Oil Well Perforators
Used by oil companies to get oil wells to yield oil.
Oil well perforators are fired radially from the well bore through the cement well bore casing and into the oil-bearing rock.
Generally, the deeper the penetration the greater the amount of oil that flows and hence the greater the return on the investment in drilling.
Literally millions of perforators are fired every year.
The mechanism how the jet is formed is described very well in G.K. Batchelor’s classic text ‘An Introduction to Fluid Mechanics.’

## Slide 24: Perforator Jet Formation
z1
zS
Casing
Explosive
Liner
Jet
z

## Slide 25: ODEs Governing Jet Formation
The time refers to time at the stagnation point S at .
The element initially at travels to reach at time
The functions depend on the thicknesses of the liner, casing and explosive taken in a direction normal to the liner, a constant specific energy , the ‘Gurney Constant’, and the liner projection velocity. [More on this later.]
The speed and projection direction of the collapsing liner are functions of the detonation speed

## Slide 26: Jet Properties
The equations of the incompressible mass and momentum conservation laws in fluid flow are used relative to the moving stagnation point (See Batchelor) to determine the radii and speeds of the jet and slug relative to the stagnation point.
The absolute speed of the jet is , where is the incoming speed with which the liner approaches S. The absolute speed of the slug is .
With the density of the liner material the penetration of the jet can be calculated.
Once again, relatively simple ODEs offer an extremely useful mathematical model for the important industrial application of formation of oil well perforator jets. Remarkably only two equations are needed.

## Slide 27: Chemical Reactions
A single simple chemical reaction is typically modelled by a kinetics equation of the form:
.
Here is the extent of reaction, with corresponding to the unreacted state and corresponding to the fully reacted state, is time, is activation energy, is the universal gas constant, and the absolute temperature.

## Slide 28: Models of Kinetics - 1
Various forms of the function are used, in an attempt to represent the progression of the reaction realistically.
A very simple one, perhaps the simplest, is
The constant is known as the pre-exponential constant.
As the reaction nears completion, i.e. as
A criticism of this form is that the reaction never actually reaches completion, but asymptotes towards it.

## Slide 29: Models of Kinetics -2
Most real chemical processes have many reactions onging simultaneously.
Products of one reaction form the fuel for subsequent reactions.
Typically the reactions are highly coupled.
Under these circumstances it is common to work with mass fractions , of the N different constituents occurring throughout the entire history of the reaction.
At any time

## Slide 30: Multiple Step Reactions
Equations are typically of the form:

## Slide 31: Example Reaction Models
Vyazovkhin et al. present a useful review of widely used kinetics models, with information of how to implement them in numerical codes.
An example from my work on explosives safety – HMX:

## Slide 32: Powder Coarsening Model
PETN is both an explosive and heart drug!
PETN is required to have a high specific surface area (SSA) to facilitate the desired reactions in both applications, and therefore, is manufactured with a small average particle size.
High surface area PETN is thermodynamically unstable (high Gibbs Free Energy) and coarsens undesirably with time through evaporation and condensation.
An understanding of PETN growth processes is required in order to predict changes, both in the loose powder, and more importantly when it is compacted as an explosive or drug.
Loose powder is simpler to model than compacted powder.
Maiti and Gee’s simple condensation-evaporation model has been incorporated by AWE into the MAGIC (FORTRAN) code.
Output from MAGIC has been compared with previously obtained experimental data.

## Slide 33: Expt: Specific Surface Area by Lötzsch Permeammetry
PETN Heating Study - SSA vs Time at 98°C
Initial rapid particle growth
Particle size equilibrium reached

## Slide 34: Scanning Electron Microscopy
0 hours
18 hours
0.5 hours
Significant growth in initial ½ hour
Large angular tetragonal crystals develop eventually (nb. not very spherical!)
High SSA and small “blocky” particles.
Reduction in SSA & increase in particle size.
Much reduced SSA & significant increase in particle size. Tetragonal crystals.

## Slide 35: The Maiti and Gee model
The Maiti and Gee model
  assumes spherical, detached particles
  assumes the driving force behind coarsening process is evaporation - condensation, driven by the Gibbs-Thompson effect.
The Gibbs-Thompson Effect
Take a collection of spherical particles of varying sizes
Small particles with higher degree of curvature have a higher vapour pressure
  Molecules detach from a particle surface, diffuse through the gas phase and condense of the surface of a different molecule.
  Over time, the larger particles increase in size, at the expense of the smaller particles which eventually disappear.
r = radius of particle
Pr = equilibrium pressure of particle, radius r
P∞ = equilibrium pressure of bulk PETN
ν = volume of molecule in the solid phase
σ = surface energy density
T = temperature
k = Boltzmann constant
Gibbs - Thompson
Notes: Gibbs-Thompson Effect refers to variations in vapour pressure across a curved surface. Small particles with a high curvature will have a higher vapour pressure than larger particles with low curvature (Ostwald-Freunlich)
Molecules break away from the surface of the small particle. Will then attached to whichever particle they come into contact with, but more likely to stay attached to a larger one. Over time, large particles increase in time, and small particles shrink and eventually disappear

## Slide 36: Mathematical Model
Equations derived by Maiti and Gee
  Net addition of molecules per unit time from the surrounding gas phase onto a particle of radius rj (j=1,2,….N) is given by:
  And rate of change of radius is given by:
Ref: A. Maiti, et al., PETN Coarsening - Predictions from Accelerated Aging Data. Propellants, Explosives, Pyrotechnics, 2011. 36: p. 124 - 130.
Assuming N sets of {Nj} particles with radii {rj}
and where:
m = mass of a PETN molecule
s = size independent roughness factor
Peq = equilibrium pressure
α =
Notes: Starting with Gibbs Thompson as the basis, Maiti and Gee have derived equations to govern the change in particle size with time.
Equation (1) governs the net addition per unit time of molecules from the surrounding gas phase, onto a particle of radius r.
Equation (2) gives the rate of change of the radius of a particle and this is the basis of programme MAGIC

## Slide 37: Gibbs-Thompson and Equilibrium Pressure
Gibbs Thompson can be rewritten as
Mass conservation implies
Hence

## Slide 38: Coarsening Modelled by ODEs
To predict time the evolution of particle size of PETN bulk powder, these equations are solved using a variable time step Runge-Kutta scheme developed in FORTRAN.
This provides a particle size histogram for each time step.
SSA at each step is then calculated using:
(3)
Ref: A. Maiti, et al., PETN Coarsening - Predictions from Accelerated Aging Data. Propellants, Explosives, Pyrotechnics, 2011. 36: p. 124 - 130.
Notes: Second order Runge Kutta - standard differential scheme.

## Slide 39: Calculated fit vs experimental fit
Constant values of s found which bound the experimental data.
No single constant value for s which enables the calculated SSA - time profile to match the experimental data.
Calculated fit, s = 0.1
Calculated fit, s = 0.007
PETN Heating Study - experimental vs calculated data

## Slide 40: Calculated fit vs experimental fit
s varied with time to minimise difference between experimental and calculated SSAs.
Calculated fit

## Slide 41: Conclusion of Powder Modelling
It has been possible to describe the experimental data using the Maiti and Gee model with a modification to incorporate time dependent surface roughness.
The result is a partially empirical fit – progress, but…
The physical interpretation of s is not yet properly understood – agreement could be fortuitous.
Further work is still definitely required to understand what goes on in a compacted explosive.

## Slide 42: Challenges
Experimental - Gain more experimental data with
  particle size determination at each time step
  varying temperature
Modelling – investigate enhancements to Maiti and Gee model to address:
  Surface diffusion
  Time dependency
  Curvature dependency
  Particle shape dependency and shape evolution
  Continuous distributions of dimension, e.g. radius to start
  Sintering (merging) of particles and awkward resulting shapes
  Loss of SSA by compaction as function of applied stress (Hertz-type problems across whole powder, permeability etc.)
Variety of modelling challenges of varying complexity – which ones matter most?

## Slide 43: Traffic Modelling - 1

## Slide 44: Traffic Modelling - 2
Consider first a simple model of a single car driving along a typical infinite straight road along the x-axis with no other traffic.
Driven by a good law-abiding driver who judges distances to perfection(!), accelerates and decelerates to comply with limits and cruises at the speed limit uniformly until he/she sees a change of speed limit.
Always seeks stopping safe distance of clear road at same limit ahead.
Speed limits start at positions for
Speed and acceleration at time

## Slide 45: Traffic Modelling - 3
Suppose , i.e. speed limit applies.
Distance to next speed limit is
If (above safe distance) then
  If then
    accelerate
  Else (
    stay at speed limit
  End If

## Slide 46: Traffic Modelling - 4
Else ( (at or inside safe distance)
  If (Speed limit decreases
    will bring speed down to correct speed limit.
  Else () (Speed limit increases)
    If then
      accelerates
    Else (
      travels at speed limit until higher limit reached
  End If
End If

## Slide 47: Traffic Modelling - 5 : Issues
Huge simplifications even for one car.
Factors missed: weather, driver error, etc.
Five ODEs depending on situation, even in this simple model.
If integrating numerically with a timestep, the time of an event like reaching a new limit may not and in general will not coincide with one of the times of the simulation.
Usually solved to a good approximation by linear interpolation if the timesteps are small enough.
Event based simulations sometimes used. Could possibly be done for simple constant accelerations but not so easily where there is dependence on speed or other variables, or when extra cars are added.

## Slide 48: Staff Modelling
Consider a two-tier company, with managers at the upper grade and workers at the lower grade.
We suppose the company is large enough to allow modelling staff levels with ODEs. These days part-time work means fractions of people are not meaningless!
Let there be workers and managers.
The company recruits staff, loses staff to other careers and retirement, promotes from grade 1 to grade 2, sacks staff at both grades, and demotes staff from grade 2 to grade 1.

## Slide 49: A Possible Staffing Model
Recruitment
Demotions From 2
Leavers
Promotions to 2
Sackings

## Slide 50: Staff Modelling - Issues
This again is a very simple model
Fractions are likely in reality to depend on .
If there is dependence on the rates of change, particularly if this is nonlinear, then determination of requires the solution of implicit equations.
The generalisation of the Newton-Raphson Method offers one possible solution method.
Depending on the equations simple iteration may converge to a solution.

## Slide 51: 4th Order Runge-Kutta Method
All of the above mathematical models have led to the requirement to solve the following set of ODEs in variables
Subject to the initial conditions
The functions may have had to be found by solution of an implicit equation.

## Slide 52: 4th Order Runge-Kutta Method for Multiple States
Define and
We may calculate at from at using the following method:

## Slide 53: Comments on the Runge Kutta Method
Robust method
4th-order accurate is great for most ODE applications. On MATLAB etc.
Combined with variable time-step methods it is very flexible.
I have also found second-order Runge-Kutta methods useful particularly in solving partial differential equations (see exercise and next lecture).
References:
  Alan Jeffrey, Linear Algebra and ODEs, Blackwell Scientific Productions (1990)
  Dennis G. Zill, A First Course in Differential Equations, 8th. Ed. Thomas Book (2005)
  More rigour: U.M. Archer and L.R. Petzold, Computer Methods for ODEs and Differential-Algebraic Equations, SIAM, Philadelphia (1998).

## Slide 54: Dynamic Friction
For surfaces sliding over each other
for V ;
for V.
F

## Slide 55: Static Friction
For sticking surfaces
for ;
for .
F