## Slide 1: Methods of Industrial Mathematics – Session 2
Extended LTCC Advanced Course – Feb-Mar 2018
John Curtis, UCL Mathematics Department
© British Crown Owned Copyright 2018/AWE.

## Slide 2: Session 2
A reminder of the diffusion equation.
Applications including heat transfer and diffusion of substances.
Common boundary conditions.
Some analytical solutions in steady state and time-dependent cases.
Numerical solution schemes including finite differences.
Brief introduction to the finite element method describing the huge role of the latter in engineering.

## Slide 3: Industrial Mathematics Encountered by JC
INDUSTRIAL MATHEMATICS USED BY JC
MECHANICS
CHEMISTRY
SIMULATION
ELECTROMAGNETIC THEORY
CONTROL THEORY
SIGNAL PROCESSING
OPTIMISATION
Arrows join most of the above subjects
N.B. No attempt at definitive list of Industrial Mathematics , e.g. Image Processing, Big Data, Formal Methods, Financial Mathematics are missing.
STATISTICS
PROBABILITY
NUMERICAL ANALYSIS
APPLIED PHYSICS
ENGINEERING
HEAT TRANSFER

## Slide 4: The Diffusion Equation
3-D
2-D
x
y
z
1-D

## Slide 5: Diffusion Equation – Applications
Heat transfer – derivation to come.
  Heat flow from higher temperature locations to lower temperature locations
Very slow diffusion of substances, e.g. air from a tyre.
  Slow flow from high concentration to low concentrations.
Diffusion of probability of crime.
Financial mathematics

## Slide 6: Derivation (1-D) - 1
Flux Equation (e.g. Fourier’s Law for heat conduction, Fick’s Law for diffusion)
< 0
> 0
A

## Slide 7: Derivation (1-D) - 2
Consider element between and .
Flux in positive -direction at at time is
Flux in positive -direction at at time is .
Rate of gain of heat between and is .
Rate of internal heat generation in element is .
Hence to first order in :
=

## Slide 8: Derivation (1-D) - 3
Using Fourier’s Law and dividing by
This is the familiar heat equation.
In the steady-state it requires boundary conditions only; otherwise both initial and boundary conditions are required.

## Slide 9: Common Boundary Conditions
Dirichlet or prescribed :
Neumann or prescribed flux ( is normal to domain in which diffusion eqn. holds):
Robin or Mixed (e.g. Newton’s Law of Cooling:
Radiation (Heat)
= 0
= 0

## Slide 10: Steady-State
Dependence on only so in 1-D:
General solution is simple:
where are constants found by use of the boundary conditions.

## Slide 11: Two Dirichlet Conditions

## Slide 12: One Dirichlet, One Flux Condition

## Slide 13: One Dirichlet, One Robin Condition

## Slide 14: One Dirichlet, One Radiation Condition - 1
where is the correct root (physically sensible) of
and .

## Slide 15: One Dirichlet, One Radiation Condition - 2
The quartic for will require solution by a method such as bisection, the Newton-Raphson method, or iteration.
Newton-Raphson converges quickly, but care in choosing sensible guessed first roots is important.
For equations in a single variable bisection is usually robust but can be slow. Again sensible initial upper and lower bounds are needed.
The equation is of the form . Often iteration is a quick and effective method for this type:
  Choose a first guess for namely
  For get the next iterate by setting
  .
  Continue until converged!
    e.g. where is a chosen small tolerance (allows zero as initial choice of ).
  This often works well, but is not guaranteed to converge – as before a sensible first choice is important.

## Slide 16: A 1-D Model of a Fin - 1
Heat generation in an element in this instance is negative - the loss by convection:
Steady-state heat equation becomes
A
P
cf. Holman (1981)

## Slide 17: 1-D Model of a Fin - 2
Put .
, where
Boundary conditions are:
CASE 1 – Semi-infinite fin
CASE 2 – Insulated end at
CASE 3 – Convection at end as well as at sides – most realistic!

## Slide 18: 1-D Model of a Fin - 3
General Solution
CASE 1
CASE 2
  B.c. give:

## Slide 19: 1-D Model of a Fin - 4
CASE 2 (cont.)
  Whence it is easily shown
CASE 3 – An exercise on sheet 2.
IN ALL CASES
  Heat dissipated by fin .

## Slide 20: 2-D Steady-State – A Special Solution - 1
No internal heat generation
Seek solution
,

## Slide 21: 2-D Steady-State –Special Solutions - 1
Separation of variables
Solution for

## Slide 22: 2-D Steady-State –Special Solutions - 2
Solution for
With a similar solution for .
Analytical solutions like this are of limited application directly but they can be very useful for checking numerical codes with non-trivial test cases.
Obviously the boundary conditions must be compatible with the above solutions.

## Slide 23: Time-Dependent Heat Conduction – The Slab -1
Consider an effectively infinite slab occupying
It is heated by maintaining the temperature at at for
The wall is fully insulated.
It is initially at room temperature .
This is effectively a one-dimensional time-dependent problem.

## Slide 24: The Slab - 2
Set .
Seek solution by separation of variables:
Then set
The minus on the right allows satisfaction of the boundary conditions.
.

## Slide 25: The Slab – 4
The general solution that can possibly fit the boundary conditions is the Fourier series
where the and are constants.
The zero flux condition at requires
The constant Dirichlet condition at requires the terms in to vanish which in turn requires
So
for even and > 0; , with odd.

## Slide 26: The Slab – 5
The solution is thus
The are found by using the initial condition and the orthogonality relationship:

## Slide 27: The Slab – 6
The full solution is thus

## Slide 28: The Slab - 7
Carslaw and Jaeger gives this solution and show how the temperature as a function of evolves with time.
The figure shows the evolution schematically.
Actual calculation for another case in a moment.
0
TIME

## Slide 29: Heat Conduction
THE Book is Carslaw and Jaeger, which gives a host of solutions for different geometries and boundary conditions (including the slab problem we have just done).
Astonishingly the solutions were undertaken by hand calculation – probably using mechanical adding machines.
The special solutions presented in such detail remain a permanent means of validating today’s numerical codes – I have used the book for just this purpose for a spherically symmetric problem (to come)

## Slide 30: Cylindrical and Spherical Polars with Symmetry
Two much used operators.
Cylindrical polars with axisymmetry:
Spherical polars with spherical symmetry:

## Slide 31: Heating of Sphere from Room Temperature by Applying Higher Temperature at Surface
This is the example I have used myself in developing a model of the reaction of a sphere of explosive whose surface is held at a fixed temperature.
Carslaw and Jaeger plot non-dimensional temperature against non-dimensional radius at non-dimensional times.
Solution is essentially the same for any material, any imposed temperature!
There is an analogous solution for a cylinder.

## Slide 32: Finite Difference Schemes for the Diffusion Equation.
The special solutions in Carslaw and Jaeger and other texts are invaluable in many cases.
However, sometimes – most times really – problems arise for which there is no special solution.
An example is where the body heating function we introduced earlier takes an awkward form – the Arrhenius reaction term, where one is also solving for the evolution of the reaction, is an example.
There is choice of numerical solution schemes available.
I have used explicit finite differences and the finite element method and reviewed implicit methods used on diffusion problems in my work in industry – but would not want to be dogmatic about choice of method.
Nonetheless, the examples which follow should give you the flavour of this kind of work.

## Slide 33: Finite Difference Scheme - 1-D - 1
March forward in time starting at then successive times
Timesteps
At time , divide spatial interval in which equation is to be solved into sub-intervals.
Use nodes, equal distances apart.
is one boundary node.
Node is the other end.

## Slide 34: Finite Difference Scheme - 1-D - 2
Expand in Taylor Series about .
Define .
Spatial expansions are:
(1)
(2)

## Slide 35: Finite Difference Scheme - 1-D - 3
Subtracting (2) from (1):
Whence
This is an approximation for the first spatial derivative valid to first order in

## Slide 36: Finite Difference Scheme - 1-D - 4
Adding (1) to (2), we get:
Whence
This is an approximation for the second spatial derivative also valid to first order in

## Slide 37: Finite Difference Scheme - 1-D - 5
Expand in Taylor Series about .
(3)
(4)
It is not uncommon to use the zero-th order approximation for the first derivative in time:

## Slide 38: Finite Difference Scheme - 1-D - 6
This seems odd given that it is not too difficult to set up a Runge-Kutta scheme to higher accuracy.
Anyway the most common explicit discretisation of the one-dimensional heat equation resulting is:
Ozisik is a good readable reference. It gives a proof that for stability of this scheme i.e. must be kept small enough.
The wise user checks for convergence by reducing his or her time-steps and checking the results are sufficiently close.

## Slide 39: Finite Difference Scheme - 1-D - 7
A common alternative is the so-called implicit or backward difference method.
This method exhibits very great stability even for much larger time-steps, at cost of requiring matrix inversion to find the values at time .
Note the user still needs to check for convergence of his or her result – stability does not always imply accuracy.
Other hybrid methods interpolate linearly between the fully explicit and fully implicit methods – I have never tried these.

## Slide 40: Finite Difference Scheme - 1-D - 8
Different approximations to flux boundary condition at e.g. node 1
Zero-th order:
First order:

## Slide 41: Symmetric Spherical Polar Schemes
Explicit scheme:
Here is the -th radial node, with at the centre.
The corresponding implicit scheme is:

## Slide 42: Finite Differences – Some Drawbacks
If the geometry of the solution domain is not easily made coincident with the mesh then there is a need for special treatment at places where the boundary cuts across the mesh.
This kind of situation can lead to inaccuracies, because difference operators with unequal arms are needed to approximate the boundary conditions.
Coding becomes very messy – application of the boundary conditions can be very complicated, especially in 3-D.

## Slide 43: The Finite Element Method (A Quick Look)
The finite element method can offer a convenient way of addressing such situations.
It divides the field in which the equations are to be solved into separate elements.
For 2-D these can be triangular as shown or quadrilateral.
For 3-D tetragonal or hexahedronal elements.
Sizes of elements may vary.
Irregular boundaries may be as closely approximated as desired by using sufficient elements.
Typical element
Approximate Boundary
Actual Boundary
Typical Node

## Slide 44: Background
Originally applied as a non-rigorous method for structural problems.
Application to simple steady-state field problems (e.g. Laplace’s and Poisson’s equations) where variational extremum principles apply.
Piecewise polynomial approximation allowed use of the classical Rayleigh-Ritz Method for variational principles. We show an example of this.
Extended to other cases where no extremum principle applied by use of Galerkin’s and other weighted residual methods.
Applications now included time-dependent problems, such as the parabolic heat equation, Helmholtz’s equation for sound propagation, electromagnetic applications among many others.
Many mathematicians are now working on the theory and investigating extensions of it.

## Slide 45: The Finite Element Method
I will give some motivation for it and show you some example applications I have done.
The introductory text by A. J. Davies is very good. The classic text is by the originator of the method, Zienkiewicz.
We will work with elements the same size but that does not have to be the case in many applications, where often only areas ‘where things are happening’ are finely meshed.
Review Calculus of Variations first and then present a simple example from heat conduction where a variational principle exists.
How this is formulated as a Finite Element problem – indication of the link to the structural method.
Then some material showing actual work with a Finite Element Package.

## Slide 46: Calculus of Variations - 1
Minimise the functional:
Subject to Dirichlet conditions:
Consider the variation about the minimum which satisfies these boundary conditions:
, where is very small.
To first order in

## Slide 47: Calculus of Variations - 2
Here

## Slide 48: Calculus of Variations - 3
Integrate third term by parts:
Arbitrariness of and the boundary conditions yield the Euler Equation:
This to be solved subject to

## Slide 49: Variational Principle for the Steady-State Heat Equation - 1
Set and define the functional
.
So .
The Euler Equation is
,
Or
.
This is to be solved subject to boundary conditions – we look at Dirichlet conditions

## Slide 50: Variational Principle for the Steady-State Heat Equation - 2
Proof that
Since 0 and the result follows.

## Slide 51: Finite Element Formulation - 1
Divide interval into elements with (for now) equally spaced nodes apart. So .
Let the node be at .
For element from point A at to point B at introduce the interpolating shape function row matrix
,
with non-zero components defined by:
only for

## Slide 52: Finite Element Formulation - 2
Plainly corresponds to A and corresponds to B.
In element we interpolate between the values of the trial function we are putting into at A and B by writing
,
where the analogues of the displacements in structural calculations are given by
We build a trial function given by

## Slide 53: Finite Element Formulation - 3
Put this into the functional to get
because is non-zero only in element

## Slide 54: Finite Element Formulation - 4
Denoting it follows that
Thus
.
We know from the Dirichlet conditions that but that in the trial function the other values of the trial function may be freely prescribed.
In this case the variational principle allows minimisation using the Rayleigh-Ritz method.
We know our solution is the minimum of so it must be at least a local minimum of minimising with respect to all the .

## Slide 55: Finite Element Formulation - 5
Hence we solve
Only terms dependent on are

## Slide 56: Finite Element Formulation - 6
Hence
Or
(*)
where
.

## Slide 57: Finite Element Formulation - 7
Equations (*) together are of the form of a structural stiffness matrix K times the displacement vector equals a loading F, here in this very simple case the zero vector
K = F = 0.
The link of the method to structural analysis is thereby shown.
For the simple linear shape functions
=
=

## Slide 58: Finite Element Formulation - 8
In (*) we therefore have
And after manipulation(*) reduces to
This is simply the finite difference scheme for the Laplacian we saw earlier – arrived at by quite different method.

## Slide 59: Finite Element Packages
Most industrial usage of the method is in applying established commercial packages which offer helpful mesh generation and graphics post-processing – writing one’s own scheme would take far too long for industry to pay. One important code has something like 600 man years of development invested in it!
New developments once proven will tend to be included in one of the packages. But something powerful and new could break into niche areas of the market.
LS-Dyna is one I have used quite extensively. Others include NASTRAN, ANYSYS, COMSOL, FlexPDE, FLUENT for fluid dynamics etc.