## Slide 1: Methods of Industrial Mathematics – Session 3
Extended LTCC Advanced Course – Feb-Mar 2018
John Curtis, UCL Mathematics Department
© British Crown Owned Copyright 2018/AWE.

## Slide 2: Session 3
A reminder of the equations of fluid flow.
Boundary conditions.
Some useful analytical solutions used in industry.
Jets and their applications and stability.
An associated application of Bernoulli's law.
An introduction to the concept of a shock.

## Slide 3: Industrial Mathematics Encountered by JC
INDUSTRIAL MATHEMATICS USED BY JC
MECHANICS
CHEMISTRY
SIMULATION
ELECTROMAGNETIC THEORY
CONTROL THEORY
SIGNAL PROCESSING
OPTIMISATION
Arrows join most of the above subjects
N.B. No attempt at definitive list of Industrial Mathematics , e.g. Image Processing, Big Data, Formal Methods, Financial Mathematics are missing.
STATISTICS
PROBABILITY
NUMERICAL ANALYSIS
APPLIED PHYSICS
ENGINEERING
HEAT TRANSFER

## Slide 4: The Material Derivative
In fluids variables, such as e.g. velocity, density, temperature and pressure, generally depend on position in laboratory co-ordinates and on time .
Position is itself time-dependent.
Derivative of a variable is therefore given by the chain rule:
,
The material derivative is most commonly written as
Here is the velocity and .
Streamline

## Slide 5: Mass Conservation
In vector notation:
= 0
which may alternatively be written as
= 0
In Cartesian suffix notation:
Or

## Slide 6: Stress and Strain Tensors
In vector notation stress in a fluid is given by
And in Cartesian suffix notation it is given by

## Slide 7: Momentum Conservation
Here is the body force.
These are the famous Navier-Stokes equations of motion for fluid flow.

## Slide 8: Energy Conservation
Here is the thermal conductivity and is the temperature.
Rate of dissipation per unit volume
Heat per unit volume gained by conduction
Rate of gain of internal energy per unit volume

## Slide 9: Useful Analytical Solutions
Steady State Solutions
  Poiseuille flow
  Bernoulli’s Law
    Efflux from an orifice in a vessel
  Momentum integral method
    Force exerted by a jet on a wall.
Time-dependent Solutions
  Oscillatory flows
  Pinching of a cylinder between two frictionless plates

## Slide 10: Steady State Solutions. Poiseuille Flow -1
Poiseuille flow is relevant to many applications in industry where flow of viscous fluids in pipes is important.
Examples:
  Flow in oil pipe lines
  Heating and refrigeration systems
  In models of permeability – e.g. the powder ageing problem in Lecture 1 was validated by comparison with specific surface areas determined by permeammetry, which has models for permeability derived from Poiseuille Flow
  Medicine

## Slide 11: Poiseuille Flow – 2
Steady flow in a pipe of radius so terms in vanish.
No swirl so
Uniform flow so terms in vanish.
Axisymmetry so terms in vanish.
Cylindrical polars.
No-slip at pipe wall so there at .
Constant pressure gradient in axial direction .
Incompressible (= constant density) viscous flow.

## Slide 12: Poiseuille Flow - 3
reduces to simply
.
This may be integrated to give
and the no-slip condition at the wall gives
.
so the only non-zero velocity component is the axial one .

## Slide 13: Poiseuille Flow - 4
In absence of body force the momentum equation in this case reduces to
Using the constant pressure gradient assumption and our formula for in cylindrical polars, the only non-trivially satisfied momentum equation is:
.
This has the general solution
,
where and are constants. The former must be zero if a solution that is singular on axis is to be avoided.

## Slide 14: Poiseuille Flow - 5
The no-slip condition at enables the determination of the other constant:
.
Hence
and the solution is:
.

## Slide 15: Poiseuille Flow -6
The flux through any cross-section is:
.
The tangential stress at the wall of the tube is:
.
The rate of dissipation per unit volume is given by:
.
The dissipation is by heating of the fluid.

## Slide 16: Bernoulli’s Law - 1
Start from the equation for the rate of change of total specific energy per unit mass:
T
Consider the case of an incompressible, inviscid, non-conducting fluid so that
and it follows that
, .
Assume . This is OK for conservative body force fields like gravity.
Above equation reduces to:

## Slide 17: Bernoulli’s Law - 2
If we now further limit consideration to steady flow we have
.
It follows that
,
Hence on a streamline
Bernoulli proved this in 1738!
If the flow is irrotational, i.e. , then is the same on each streamline (cf. Batchelor).

## Slide 18: Bernoulli’s Law – 3: An Application
Consider the efflux of fluid with speed from an orifice at height in an open vessel.
In absence of an orifice we know the pressure depends on the height of the liquid above it.
If an orifice opens the fluid will be driven by this high pressure.
If the hole is small (or if the fluid is replenished by e.g. a ‘ballcock’) then the drop in height with time will be very small or zero.
We can usefully model the flow in the steady-state case.
All the assumptions in deriving Bernoulli’s Law apply.
Atmospheric pressure is
is the height of the free surface above the orifice.
Dimension of the orifice cross-section is very small compared with .

## Slide 19: Bernoulli’s Law – 4
The body force is gravity, so that
and hence
,
where is constant.
Assuming at the free surface in the vessel, Bernoulli’s law applied to any of the streamlines gives

## Slide 20: Bernoulli’s Law – 5
This equation reduces to
,
Whence
.
This is a useful formula to predict the speed of the emerging jet of fluid, though of course in real fluids factors such as viscosity, compressibility, heat transfer will play a part and in some cases may significantly change the result (usually reducing it).
Computational Fluid Dynamics (CFD) using finite differences, the Volume of Fluid (VoF) method or the finite element method can be used to make more detailed predictions of the flow, but setting these problems up and checking they are working correctly is usually not a rapid process.
The mass flux cannot be found by Bernoulli’s Law alone; it is usually rather less than the product of the orifice area, the density and the speed.

## Slide 21: Bernoulli’s Law – 6
In industry many vessels are pressurised so the pressure terms differ on either side of the equation.
In fact the efflux may be controlled by adjusting this pressure or changing the size or shape of the orifice.
There are analytical results available for two-dimensional flows from orifices – Batchelor describes these in more detail.
An important application is that of quickly and crudely modelling accidents where there is a breach of the vessel and a jet of fluid escapes.

## Slide 22: Momentum Integral Method - 1
Start from the momentum equation for an inviscid () incompressible () fluid in which the body force is negligible and steady –state flow is assumed, so that terms in vanish.
.
If we take the contraction (dot product) with an arbitrary constant vector and integrate over a volume of fluid we have:
.
This is easily rewritten as
.

## Slide 23: Momentum Integral Method - 2
Use of the divergence theorem on each side and collecting terms then gives:
.
The arbitrary constant nature of implies the momentum integral relation over the surface as :
We now consider a simple application of this.

## Slide 24: Momentum Integral Method – 3: An Application
Consider a 2-D jet travelling at speed impacting on a frictionless wall, with an acute angle between the jet and the wall.
Consider three surfaces far from the collision as follows:
  the cross-sectional area per unit depth of the incoming jet;
  the cross-sectional area of the flow along the wall making an obtuse angle with the incoming jet;
  and the cross-sectional area of the flow along the wall making the acute angle with the incoming jet.
Far from the impact point I at , the pressure across each jet is simply atmospheric .
Bernoulli’s Law then gives
I

## Slide 25: Momentum Integral Method – 4
At
At .
At .
At , , and , the normal velocity component vanishes: .
At .
We assume that
The non-zero terms in the 1-component of the momentum integral equation are:

## Slide 26: Momentum Integral Method – 5
The integrands are all constant so this equation reduces to
.
Mass conservation gives:
.
Hence
and .

## Slide 27: Momentum Integral Method – 6
The non-zero terms in the 2-component of the momentum integral equation are:
.
Hence the force on the wall is given by:
.
For our accident scenario of the vessel with a hole, this formula allows an estimate of the force exerted by the jet on the face of an adjacent structure:

## Slide 28: Time-Dependent Solutions Oscillatory Flows - 1
Although steady-state solutions have useful applications as we have just seen – with some more to come as we consider jets - the vast majority of flows are in reality time-dependent.
It is obviously impossible to cover everything, but here are some that have come up or been of interest in my work in industry.
Through my work on spacecraft I encountered periodic flow in a tube associated with the nutation damper for the Ulysses spacecraft. I regret I cannot show you this work as it was proprietary work, uncleared for publication.
However, we can usefully discuss some examples of oscillatory flows which give you the ‘flavour’ of the work, which as I said is the aim of this course.

## Slide 29: Oscillatory Flows - 2
Consider the two dimensional unsteady incompressible viscous unidirectional flow in the -plane set up by the sinusoidal oscillation of a rigid plane boundary moving in its own plane.
The fluid is in the domain .
Let the plane be at and oscillate to and fro in the direction with the only non-zero velocity component
We suppose the fluid has velocity
.

## Slide 30: Oscillatory Flows - 3
Incompressibility is satisfied immediately as there is no dependence of the -component of velocity.
The x-component of the momentum equation is
.
We attempt to eliminate time dependence by seeking a harmonic solution
.
Hence
.
The only finite solution is
.

## Slide 31: Oscillatory Flows - 4
Applying the boundary condition at gives
You can see how the solution decays with increasing , as you would expect.
Higher density leads to more rapid decay with increasing .
Higher viscosity decreases the rate of decay.
You can also see that the need for the oscillation to diffuse into the fluid changes the phase of the oscillation with increasing

## Slide 32: Oscillatory Flow - 5
Consider the two dimensional unsteady incompressible viscous unidirectional flow in the -zplane set up by the sinusoidal oscillation of a tube of radius moving parallel to its axis.
The fluid is in the domain .
Let the tube oscillate to and fro in the direction with the only non-zero velocity component
We suppose the fluid has velocity component in the direction given by
.

## Slide 33: Oscillatory Flow - 6
Incompressibility is satisfied immediately as there is no dependence of the -component of velocity.
The -component of the momentum equation is
.
We again seek to eliminate time dependence with a harmonic solution
.
Hence

## Slide 34: Oscillatory Flow - 7
If we write and set , then we get the Bessel Equation
,
with finite solution the Bessel function of the first kind:
.
Here the constant is a constant complex number whose value is found from the boundary condition at
Noting that ,

## Slide 35: Oscillatory Flow - 8
it follows that
.
The boundary condition requires
.
Hence

## Slide 36: Oscillatory Flow - 9
Thus
.
This can be evaluated by the appropriate Bessel function series.
Depending on the complexity this kind of problem may be best solved numerically directly.
However, analytical solutions as above can offer very valuable verification of the numerical schemes.

## Slide 37: Pinching of a Cylinder - 1
This problem arose in considering the response of explosives to being pinched by large weights.
Consider an cylinder of fluid being pinched between two frictionless plates apart.
The top one is being forced down at a constant speed and the bottom one is held stationary.
The radius increases with time.
Consider potential flow – incompressible, irrotational and inviscid.
Axisymmetry with no swirl assumed.
R(t)

## Slide 38: Pinching of a Cylinder - 2
An analytical solution is sought by putting
.
The height is given by
, where .
Mass conservation gives
.
Hence

## Slide 39: Pinching of a Cylinder - 3
Integrating we obtain
.
So
,
where is an arbitrary function.
For the radial velocity component to remain finite , so that
.

## Slide 40: Pinching of a Cylinder - 4
Momentum conservation in radial and axial directions:
,
.
With our velocity field the radial equation becomes
.

## Slide 41: Pinching of a Cylinder - 5
The axial momentum equation becomes
.
Hence .
Integrating the radial equation we have
where is an arbitrary function of
Applying the boundary condition at we get
.

## Slide 42: Pinching of a Cylinder - 6
On
.
Hence the radius of the cylinder is given by
where .
Developing this solution was a very useful precursor to developing the plastic flow solution that we needed for the explosive.

## Slide 43: Jets - 1
Jets are used in a variety of industrial applications.
Examples:
  Ink jet printers
  Oil well perforators
  Cleaning jets
  Drilling of geological materials in mining and oil recovery
  Cutting and slicing of materials including:
    Glass
    Steel
    Food

## Slide 44: Jets - 2
In many applications inviscid incompressible irrotational, i.e. potential, flow is a reasonable assumption.
Incompressibility
.
Momentum
.
In many common situations in everyday life the basic solution before considering the stability of the jet is extremely simple.
The jet travels without stretching at constant velocity and radius with no pressure gradient.
In cylindrical polars
The mass and momentum equations are trivially satisfied.

## Slide 45: Jets - 3
In some situations it is desirable to have a stretching jet.
A prime example is that of the shaped charge jet as used in oil well perforators, ejector seats, tree-felling, demolition, and military applications.
Here the penetration depends on length (as we will show later) and the longest possible jet is wanted. For oil well perforators penetration length and the financial return from an oil well are highly correlated.
The mathematics is very similar indeed to that used for the pinching of the cylinder just presented and so it is a problem on the sheet.

## Slide 46: Jets - 4
In some applications break-up of the jet into droplets is required.
Ink jet printers are the prime example of this.
Here the instability of the curved jet surface caused by surface tension is used to generate the droplets.
You see this process occurring every time you run a tap!

## Slide 47: Jets – 5: Stability
We consider the stability of a non-stretching jet in potential flow.
First note that a free surface given by the equation
must satisfy
For an axisymmetric jet having radius , the free surface is
.
Hence
.

## Slide 48: Jets - 6
This reduces to
For our steady-state solution this is identically satisfied.
The surface tension boundary condition is
,
where is the surface tension and and are the principal radii of curvature so we have , the jet radius, and

## Slide 49: Jet - 7
Hence
Let us now consider a small perturbation about the above uniform solution, which we denote as the zero-th order solution with superscript (0) henceforth, the perturbation being denoted by (1).
Denoting the potential by we set

## Slide 50: Jets - 8
It is convenient now to work in a frame moving with the speed of the unperturbed jet.
In this frame .
The pressure boundary condition and free surface condition are expanded about using Taylor Series.

## Slide 51: Jets – 9: Conservation of Mass and Momentum
To first order mass conservation is
.
The momentum conservation equations are

## Slide 52: Jet – 10: Pressure Boundary Condition
We have
.
To first order the pressure boundary condition is therefore:

## Slide 53: Jets - 11
The first-order free surface condition is
on
We now seek a sinusoidal perturbation of the undisturbed jet by writing:
.
Here we save time by picking the phases of the perturbations so as to be consistent.

## Slide 54: Jets - 12
To first order must satisfy
.
This is
with general solution:
,
where is a Bessel Function of the second kind and is an as yet arbitrary function of time.
Recall in potential flow

## Slide 55: Jets – 13
Hence
,
.
The free surface condition then yields:
Thus
.

## Slide 56: Jets - 14
The pressure boundary condition at first order becomes
.
The z-component of the momentum equations reduces to
.
And hence
.
Using the boundary condition for above we have

## Slide 57: Jets - 15
.
Eliminating in favour of we obtain after manipulation the equation governing the growth of the sinusoidal disturbance originally derived by Lord Rayleigh:
.
The fastest growing or dominant wavelength that eventually leads to droplet formation (as in printer ink jets) is found by maximising
with respect to

## Slide 58: Jets – 16: Jet Penetration
The penetration of jets is very important in numerous industrial applications.
In many cases it has been found possible to use the theory of incompressible inviscid flow, basically because for high speed jets viscosity is negligible and for many metals the effects of compressibility are negligible or nearly cancel.
We present the incompressible theory based on Bernoulli’s Law.
Note that there is a an analogous compressible theory based on the compressible version of this Law.

## Slide 59: Jets – 17: Penetration Using Bernoulli’s Law
For high speed jets travelling at speed in the km/s regime the influence of gravity is negligible.
In the steady state Bernoulli’s Law is simply
.
To predict penetration speed Hill Mott and Pack applied this Law in a frame moving with the axial point P at the interface between jet and target.
It turns out that the steady flow assumption works well even for jets with a gradient of velocity along them.
P

## Slide 60: Jets – 18: Penetration Using Bernoulli’s Law
In the frame moving with P at velocity far from P the jet is travelling at and the target with velocity .
The pressure far from P is taken as atmospheric pressure
At P itself both are at rest in this frame: in both jet and target and the pressures are equal just to the left and right of P (lest there be infinite acceleration happening!).
Let be the pressure at P, the S standing for ‘stagnation’, as in this frame P is sometimes referred to as the ‘stagnation point’ even though it is actually travelling at several km/s!
Then, applying Bernoulli’s Law along the axis, we have in the jet of density :
.

## Slide 61: Jets – 19: Penetration Using Bernoulli’s Law
Similarly in the target of density :
.
Elimination of yields:
.
This results in the quadratic for
with physically possible solution
.

## Slide 62: Jets – 20: Penetration Using Bernoulli’s Law
Let a jet element of length take a time to penetrate a distance
Then
.
It follows from the solution just found for that:
.
This is the famous hydrodynamic penetration law of Hill, Mott and Pack.
For a jet of uniform speed and length L the total penetration is simply
.
We explore what happens for stretching jets in one of the sheet questions.

## Slide 63: Shocks - 1
Shocks arise under conditions where there is impact or sudden release of energy such as when an explosive explodes.
Typical impact speeds causing shocks are in the range
500 – 10,000 m / s.
Pressures are in the GPa regime, usually dwarfing material strength, so that the material (even a metal) responds like a compressible fluid.
When shock waves hit the surface of a dense material they are reflected back at even higher pressure – the reason why e.g. the aircraft fuselage was ruptured in the Lockerbie disaster.

## Slide 64: Shocks - 2
Shocked Pre-shock
Density
Particle Velocity
Pressure
Internal energy
SHOCK

## Slide 65: Shocks – 3: The Rankine-Hugoniot Equations
Derived by considering conservation of mass, momentum and energy in a frame moving with the shock travelling at speed .
Courant and Friedrichs gives derivations and a wealth of information on shocks.
Mass:
.
Momentum:
.
Energy:
.

## Slide 66: Shocks - 4
These are 3 equations in 4 unknowns for the shocked variables.
An extra equation is required to close the system.
Often the empirical ‘Shock Velocity/Particle Velocity’ relationship is assumed:
,
Here is the speed of sound in the pre-shocked state, and is the empirically determined constant.
More rigorously the system can be completed by using the ‘Equation of State’. This is usually a constitutive law for the pressure in the form:
.

## Slide 67: Some Very Significant Omissions with Industrial Application
Not presented as I have no or limited personal experience.
Boundary-layer theory – Aerodynamics, spacecraft re-entry, oceanography etc.
Turbulence – engine modelling, aerodynamics again, heating systems, the weather etc. I once (n.b. decades ago) did a review of the different models for a client, but have never applied them myself. Models to consider then included the Model, Algebraic Reynolds Stress Model (ARSM) , Large Eddy Simulation. Computing having come on immensely this one deserves a warning !
Porous flow of gases and liquids. Immense industrial importance especially in gas and petroleum recovery. Darcy’s Law.